SAFETY GUIDELINES FOR SHPB

- Never perform experiment without the help of other students

  - For ease of conducting a safe and efficient experiment

- Make sure proper precautions are made prior to experiment

  - Wear safety glasses at all times

  - Long sleeve shirts and shoes should be worn,  no open toe shoes or sandals

  - Make sure all wires and gages are adhered correctly and prepared properly

- Make sure proper bars are being used depending upon specific materials being tested (steel or aluminum bars)

  - Solid-Solid Bar (hard materials)

  - Solid-Hollow Bar (soft materials)

  - Hollow-Hollow (real soft materials)

- DO NOT PRESSURIZE GUN UNTIL YOU ARE ABOUT TO FIRE

  - Do not put fingers between bars, i.e. striker and incident bar or incident and transmitter bar when SHPB is pressurized

  - Do not stand in front of muzzle or try to load striker bar when pressurized

  - Do not leave bar unattended after pressurized

  - If adjustments are needed, vent the pressure beforehand

- Conduct yourself in a mature and responsible manner at all times in the laboratory

- Make sure to yell “firing” when experiment is about to be run and SHPB is being pressurized, keep outside doors closed so no one walks in

- Make sure everyone in the lab, helping or not with the experiment,  is aware an experiment will be taking place